## Slide 1: Cansolair Efficiency Monitoring System
Progress Update by: Dylan Stone

## Slide 2: Cansolair
30 Year old Canadian company
This solar heater is their primary product
Solar Air Heater
Uses the sun to heat internal air
Uses a fan to circulate the air through the system
Located at NSCC
$2000+

## Slide 3: Monitoring System
Power Calculation
Flow Rate
Temperature Differential

## Slide 4: Raspberry Pi
Raspberry Pi 3
A tiny computer
GPIO header
Model with the most features

## Slide 5: Temperature Sensors and Flow Rate
DS18B20 Digital Temperature Sensors
Accurate to a 16th of a °C
One-Wire Bus protocol
Can Be Wired in parallel
Only need Power, Ground, and Data
Flow rate was determined using a Hot Wire Flow Rate Sensor
Only need one Flow Rate measurement

## Slide 6: Vent And IR Sensor
Vent with flap that opens to exhaust air
Infrared sensor across the flap
Outflow temperature sensor

## Slide 7: Real Time Clock
Raspberry Pi clock loses time with power
DS1307 RTC
Uses I2C Protocol
Simple to set up
Automatically syncs time
Disables Pi Clock

## Slide 8: Circuit Board

## Slide 9: Program
Python language
Takes measurements once a minute when the vent is closed
Takes measurements about every 4 seconds when the vent is open
Calculates power and energy
Logs to a spreadsheet
Logs a second file with total kWh per day
USB Saving and flow rate adjustment
Automatically launches on boot

## Slide 10: Program Flow
Read each temperature
Calculate power if the vent is open
Make a string using all the data
Save the string to a .csv file
Print the data
Checking the vent and for a USB Drive periodically

## Slide 11: Problems Encountered
Learning to use Linux
Learning python
Flow rate
Circuit Board
USB Saving
Energy calculation time differential
Launching on boot

## Slide 12: Data

## Slide 13: Data

## Slide 14: Data

## Slide 15: Acknowledgements
Glenn Macleod
Steve MacCarron
Alain Joseph
James Thomson
Dale Jollimore

## Slide 16: Demo and Questions